## Slide 1
Lighting:
Operation & Safety
Spring 2016

## Slide 2: Before Borrowing Lighting Kits
Complete the online quiz
Score 100% based on the material in this workshop
Show the library technicians
Get a sticker for your student card
Lighting Kits
https://www.lib.sfu.ca/about/branches-depts/fraser/fraser-equipment/siat-equipment

## Slide 3
https://www.lib.sfu.ca/about/branches-depts/fraser/fraser-equipment/siat-equipment
Quartz Halogen vs. Incandescent Lighting
  Both operate on the same principle:
    Electric current passes through a thin tungsten metal filament causing it to heat white hot and emit light
  However, quartz halogen lamps encase the filament in a quartz casing filled with halogen gas. This allows these bulbs to run hotter, brighter and whiter
Lighting Kits

## Slide 4
Lighting Kits For Loan:
  Small Lighting Kit
    3 x Lowel Prolight 150W tungsten balanced lights
    Low-level key or accent light, fill light (with diffusion) or back-light for interviews & other small shooting-areas
    3 x stands
    3 x barn doors
    Colour correction and diffusion gels
Lighting Kits
https://www.lib.sfu.ca/about/branches-depts/fraser/fraser-equipment/siat-equipment

## Slide 5
Lighting Kits
Lighting Kits For Loan:
  Large Lighting Kit
    Contains one 750W ARRILite open face lamp and two 300W ARRI fresnel lamps
    Ideal for lighting standing or multiple subjects or from a farther distance
    3 x stands
    Soft-box
    3 x barn doors
    Scrims
https://www.lib.sfu.ca/about/branches-depts/fraser/fraser-equipment/siat-equipment

## Slide 6
Lighting Kits
Safety
  Check all equipment for damage before use
  Tape down all cables with Gaffer tape or duct tape (the library can provide duct tape)
  Use in dry conditions
  Always open the barn doors before turning a lamp on
  Use at least 14 gauge extension cords
  Never look directly at the lamps (call “Spark!”)
https://www.lib.sfu.ca/about/branches-depts/fraser/fraser-equipment/siat-equipment

## Slide 7
Lighting Kits
Safety
  Never pick up and move a lamp stand while the lamp is on
  Do not operate the lamps pointing up or down at a very steep angle
  Do not operate lamps upside down; they could overheat
  If smoke appears around the lamp or cables turn off the lamp and return it to the library
https://www.lib.sfu.ca/about/branches-depts/fraser/fraser-equipment/siat-equipment

## Slide 8
Lighting Kits
Hot Lamps
  These lights can get very hot!
    Use only approved accessories and gels that are specifically designed for use with hot lights.
    When placed on or very near the lights, any other materials such as paper, plastic or cellophane will melt and possibly ignite.
    If you have a problem with a bulb, DO NOT attempt to change it, return it to the library for assistance
    Subjects will be affected by the lights; consider their comfort
https://www.lib.sfu.ca/about/branches-depts/fraser/fraser-equipment/siat-equipment

## Slide 9
Lighting Kits
Hot Lamps
  Keep all subjects/objects minimum 2 meters away
  Keep all lamps and cables at least 6 meters away from all flammable materials such as gas and oily rags
  Do not touch the lamps without gloves for at least 5 minutes after turning them off
https://www.lib.sfu.ca/about/branches-depts/fraser/fraser-equipment/siat-equipment

## Slide 10
Lighting Kits
Electric Safety
  How to find the draw on a circuit
    Draw (amperage) = total light wattage (watts) / voltage
– e.g. draw = 1000 watts / 120 volts = 8.3 amps
    In North America, 120V is the standard
    Most households have 15amp circuits
    Using this formula do not load a circuit more than 80% of its maximum
- e.g. most household circuits are rated at 15 amps:
» 15 amps x 80% safety factor = 12 amps
» (do not use more than 12 amps)
https://www.lib.sfu.ca/about/branches-depts/fraser/fraser-equipment/siat-equipment

## Slide 11: W
Lighting Kits
12amps=
W
120volts
A= V
https://www.lib.sfu.ca/about/branches-depts/fraser/fraser-equipment/siat-equipment

## Slide 12
Lighting Kits
W=12amps
W=AV
x 120volts =1440watts
approx. 1440w of lights may be loaded on a standard household circuit
https://www.lib.sfu.ca/about/branches-depts/fraser/fraser-equipment/siat-equipment

## Slide 13
Lighting Kits
Activity: Inventory Check
  What is in the Kit:
    A set of 3 lamps
    3 sets of barn doors
    3 light stands
    Operation and safety guide
    Gaffer’s tape or duct tape
    Leather gloves
    Gels and clothes pegs are in the Small Lighting Kit only
    Soft-box and scrims are in the Large Lighting Kit only
https://www.lib.sfu.ca/about/branches-depts/fraser/fraser-equipment/siat-equipment

## Slide 14
Lighting Kits
Activity: Inventory Check
  Additional items you should borrow from the library
    Gels (not in the Large Lighting Kit)
    Sandbags
    Umbrellas, reflectors, bounce boards, gobos
    14 gauge power extension cables
    Duct tape
  Ask the library techs for accessories!
https://www.lib.sfu.ca/about/branches-depts/fraser/fraser-equipment/siat-equipment

## Slide 15
Lighting Kits
http://www.libsfu.ca/surrey/equipment
Extras You Can Supply:
  Wooden clothes pegs for fastening gels, foils, etc.
  Practical lighting from hardware stores:
    Utility lights:
– Aluminum reflectors, ceramic sockets, etc.
    Windshield sunscreen as a reflector
    Foam core whiteboard
    Leather gloves for handling bulbs
https://www.lib.sfu.ca/about/branches-depts/fraser/fraser-equipment/siat-equipment

## Slide 16
Lighting Kits
Activity:
– Setup and Assembly
https://www.lib.sfu.ca/about/branches-depts/fraser/fraser-equipment/siat-equipment

## Slide 17
Lighting Kits
Assembly and Setup
  Procedure:
    Assemble your lighting kits according to the instructions
    Recall what you learned about safety and…
    Set the lights according to the 3-point lighting diagram
    After your setup is checked by your instructor, disassemble
and return the kits
https://www.lib.sfu.ca/about/branches-depts/fraser/fraser-equipment/siat-equipment

## Slide 18
Lighting Kits
Online Quiz:
  https://www.lib.sfu.ca/about/branches-depts/fraser/fraser-equipment/siat-equipment
    Lighting kit workshop and quiz
https://www.lib.sfu.ca/about/branches-depts/fraser/fraser-equipment/siat-equipment

## Slide 19
Lighting Kits
Questions:
  Contact the Library Media Technicians
    fraser_library@sfu.ca
    778-782-7411
https://www.lib.sfu.ca/about/branches-depts/fraser/fraser-equipment/siat-equipment